## Slide 2: Wenger road BRIDGE reconstruction PROJECT, clt-20-206
Notes: Provide presentation summary verbally:
Project location
Ex structure details
Project scope
Ex condition
Right-of-way
Project costs
Project schedule
Maintenance of traffic

## Slide 3: Aerial View
NORTH
PROJECT
LIMITS
HOKE RD
WENGER RD
UNION BLVD
I-70

## Slide 4
CLT-20-206
PEDESTRIAN BRIDGE
Aerial View
NORTH

## Slide 5
Date Built: 1988 (no prior rehab)
Intersecting Feature: Moss Creek
Superstructure Type: Prestressed Concrete Box Beams
Span Length: 39 feet (single span)
Structure Width: 32 feet (two lanes of traffic)
Existing Structure details

## Slide 6
Superstructure replacement
Patching and sealing concrete surfaces
Rock channel protection improvement
Minimal roadway profile work
Guardrail replacement
PROJECT SCOPE

## Slide 7
On the roadway looking East over the bridge
Bridge profile looking North
EXISTING CONDITION

## Slide 8
The over-the-side deck drainage along both the South and North edges has deteriorated significantly. The drip edge is rusted and perforated along the whole length for both sides and the waterproofing membrane is falling off or completely missing along most of the Southern edge. This condition will be resolved with the proposed superstructure replacement.
EXISTING CONDITION

## Slide 9
Large areas of delamination on the walls of both the East and West Abutments will be removed and patched as part of the proposed project.
EXISTING CONDITION

## Slide 10
Of the 8 total beams, beam #2 is in the worst condition with over 16 sqft of combined spalling, delamination, and exposed strands. Overall, the deck and superstructure were rated in Poor Condition and will be removed and replaced as part of this project.
EXISTING CONDITION

## Slide 11
Deterioration of nearby beam #3
Delamination and spalling of beams #6 & 7
EXISTING CONDITION

## Slide 12
ADJACENT PROPERTIES & RESPECTIVE OWNERS
NORTH
Temporary R/W
Utility Easement
No R/W Impact
LEGEND

## Slide 13
Acquisition of 0.021 acres of Temporary Easement from Parcel 2 on the north-west side of the road is necessary for access to the bridge for construction.
TEMPORARY RIGHT-OF-WAY
PARCEL #2 – M57-00721-0002 – deeter et al.
NORTH

## Slide 14
TEMPORARY RIGHT-OF-WAY
PARCEL #2 – M57-00721-0002 – deeter et al.

## Slide 15
UTILITY easement
PARCEL #5 – M57-00714-0004 – St. paul catholic church
NORTH
Acquisition of 0.038 acres of Utility Easement from Parcel 5 on the south-east side of the road is necessary for AES utility deconfliction within the construction limits.

## Slide 16
UTILITY easement
PARCEL #5 – M57-00714-0004 – St. paul catholic church

## Slide 17
Design: MCEO design in-house
Right-of-Way: TBD by real estate appraisal
Construction:
PROJECT COSTS
$ 389,800.00
The MCEO has obtained an LTIP grant through the OPWC for $195,000.00 to be applied to eligible project costs

## Slide 18
PROJECT SCHEDULE
Design: April 2021 – May 2023
Right-of-Way: July 2023 – December 2023
Advertise & Award: January 2024 – February 2024
Construction: March 2024 – May 2024

## Slide 19
Maintenance of traffic
Road closure for 30 working days March 2024 - May 2024
Notice sign will be in place 21 days in advance to closure
Huls Drive will be accessible from the West
Deeter Drive and St. Paul Church will be accessible from the East
NORTH